## Slide 1: Week 4
Filters (an introduction)
Asynchronous Tasks
Image capture
Notes: Things to improve:
Confusion about copying into/out of OS-provided buffers

## Slide 2: Overview
We’ll be taking a brief look at filtering
  An indepth treatment would take many weeks
  This will be enough to cover the absolute basics
    How to use a filter
    How to create the most basic of filters
    Two methods of actually applying the filter to data
  We will NOT cover filter design
    If you want to learn this, take EE 442
      More filter design than you will ever want
      Still only covers FIR and IIR, doesn’t cover adaptive, Wiener, etc…
    For the curious, the only filter design we’ll touch is windowed FIR

## Slide 3: Signals and Systems
Signals are collections of (sampled) data
  Timeseries such as audio
  Spacial datasets such as images
Systems are objects which manipulate signals
  Typically characterized by their “input/output” relationships
  In the diagram below, we say y[n] is x[n] passed through H
H
x[n]
y[n]

## Slide 4: Filters
Filters are systems which operate on frequencies
  They allow certain frequencies to pass through, but not others
  A “lowpass” filter allows low frequencies to pass through
  A “highpass” filter likewise allows high frequencies through
The first thing to realize is no filter is perfect
  No filter will pass everything you want while stopping everything you don’t
  Everything is a balance between different parameters you can control
We won’t study how to design filters
  We will, however, study properties of filters and how to use them
  This requires knowing what filters can and cannot do

## Slide 5: Filters – Frequency
Filters can be characterized a few different ways
  We’ll start by looking at their properties in the frequency domain
Our filters have the following freq-domain attributes:
  Passband gain and bandwidth
  Stopband attenuation
  Transition bandwidth

## Slide 6: Filters – Time
Filters are themselves characterized by a signal
This is called the “impulse response” of the filter
  We obtain those frequency-domain plots by Fourier transforming the impulse response of the filter, taking the magnitude and plotting it
The time-domain property we care about is length
  Anything else is best left to
  a Filter Design course

## Slide 7: Filtering
We apply a filter a signal via “convolution”
  Remember, a filter is really just a signal as well, an “impulse response”
  Convolution combines two signals, creating a third
I’m sure you all remember convolution:
  In discrete time, with h[n] the impulse response of the filter, x[n] the signal:
Why convolution? Where does it come from?
  The answer lies within the Fourier transform

## Slide 8: Convolution
One of the basic properties of the Fourier Transform
  “Convolution in time is multiplication in frequency”
Therefore, the Fourier Transform of y[n] is simply:
This gives us a simple intuition with filters
  They apply a scaling at each frequency
  This scaling coefficient is simply H[k], the Fourier transform of h[n]

## Slide 9: Convolution
So let’s pull apart the mathematics a bit:
This is a dot product between N-dimensional vectors
  This calculates a single output sample
  To calculate other values, just insert different values of
  Although has been reversed inside the dot product, you can reverse either or , it doesn’t affect the output

## Slide 10: Convolution
For those of you familiar with algorithmic complexity
  Convolution is not particularly efficient
  To convolve faster and better, we can use that Fourier property:
    “Convolution in time is multiplication in frequency”
  Why not just multiply to begin with!
DFT
DFT
×
IFT

## Slide 11: Circular Convolution
This performs “Circular Convolution”
  Slightly different from Linear convolution
Typically performed in windowed chunks of input
  Causes the tail end of the convolution to “wrap around” to the beginning
  Due to DFT’s periodic assumption
Be aware of this when convolving with your signal
  Windowing will take care of some of this, not all of it
  By windowing, I mean multiplication with a window function:
    Hann, Hamming, Blackman, Kaiser, etc…
Zero-padding can solve this for you!
  Zero-pad both signals to a length that will contain the entire convolution
  If you want to do this, don’t forget Overlap-and-Add!

## Slide 12: Circular Convolution

## Slide 13: Asynchronous Tasks
Let’s wash the EE stuff down with some CS concepts
C# has some more goodies for us
  Sometimes, we want to execute things asynchronously
    But we don’t want/need to do them simultaneously
Enter the async and await keywords
  The former modifies function declarations
  The latter modifies function calls
private async void myGreatFunction()
{
...
float[] result = await myOtherGreatFunction();
}

## Slide 14: Asynchronous Tasks
You must use async on any function with await in it
The await keyword tells the compiler “wait for this”
  Execution of the current function stops until done waiting
  Execution then resumes
Internally, this is making extensive use of Dispatcher
  The compiler reaches a condition inside of an await
  Execution stops, all code after the condition is given to the Dispatcher
  Eventually, the condition is cleared, and the Dispatcher continues
This is really useful for waiting for external events
  Files loading, shaders compiling, network resources arriving, etc…

## Slide 15: Asynchronous Tasks
async Task<int> AccessTheWebAsync()
{
HttpClient client = new HttpClient();
Task<string> data = client.GetStringAsync("http://msdn.microsoft.com");
// You can do work here that doesn't rely on [data]
DoIndependentWork();
string urlContents = await data;
// The return statement specifies an integer result.
// Any methods that are awaiting AccessTheWebAsync retrieve the length value.
return urlContents.Length;
}

## Slide 16: Asynchronous Tasks
All async methods return a Task
  This wraps around the desired return type
  Asynchronous methods return before their work is “complete”
  This allows synchronous methods to explicitly wait for the condition
  Only happens once you access the Result property
private void myGreatFunction()
{
Task<int> taskData = AccessTheWebAsync();
int data = taskData.Result;
}

## Slide 17: Asynchronous Tasks

## Slide 18: Asynchronous Tasks
We won’t be using them this week
We will be using them next week
  And the week after
  And the week after…
Useful when dealing with time-intensive operations
  Time-intensive: more than a few milliseconds!

## Slide 19: Image Capture
We’re going to study the absolute basics today
  We’ll follow up with a much more thorough treatment next week
At the end of this section, you will be able to
  Take a photo
  Display it to the user
  Save it to the photo library
Next week we’ll learn all the nitty gritty
  Hooking up a viewfinder
  Being able to process the preview buffer
  Controlling Flash, Focus, etc…

## Slide 20: Image Capture
We will make use of the PhotoCamera class
  Gives us a CaptureImageAvailable event we can subscribe to
  Offers a CaptureImage method we can call to take the picture
That event, triggered after calling CaptureImage, gives us a Stream full of image data
  Streams are Microsoft’s memory I/O interfaces
    Examples include FileStream, MemoryStream, NetworkStream, etc.
  We can pipe the Stream into a BitmapImage, which we can feed to XAML
  The XAML element we’ll be using is called, (surprise surprise) Image
This all must happen after Initialization, of course
  To initialize properly, we must use a VideoBrush

## Slide 21: Camera Initialization
Create a PhotoCamera that uses the back camera
cam = new PhotoCamera(CameraType.Primary);
Subscribe to desired events
  At least Initialized and CaptureImageAvailable recommended
Create BitmapImage and VideoBrush
  Hook VideoBrush up to the camera to initialize it (We MUST do this)
  Hook BitmapImage up to the Image XAML element so we can update it
bitmap = new BitmapImage();
brush = new VideoBrush();
brush.SetSource(cam);
xamlImage.Source = bitmap;

## Slide 22: Image Capture
When our CaptureImageAvailable event is called
  Just update our Bitmaps “source”
bitmap.SetSource(e.ImageStream);
This can crash, can anyone tell me why?
That’s all there is to Image Capture for now
  Last thing to do is save this image to the Photo Library
  That is something you will have to look up by yourself
    Hint: Microsoft.Xna.Framework.Media.MediaLibrary is your friend

## Slide 23: Homework 4
A two-parter!
  Part 1: Create an audio filtering app
    I will provide a FilterDesign object to create Windowed FIR filters
    Use the Slider control to set the center frequency and bandwidth
    Take input audio, filter it, spit it out
      Yes, you will be writing the filtering routines
      Straight-up linear convolution, save circular for later
    Note that logarithmic mapping will likely make your sliders more useful
  Part 2: Camera basics
    Take images in from the Camera
    Display them to the user
    Save them to the media library
  This is an excellent opportunity to learn how to have multiple apps in the same solution, please do this so your homework submission is one .zip file

## Slide 24: Misc. info for HW 4
Don’t forget to lookup all the permissions needed
  Getting “Invalid Operation” exceptions is a good indicator that you forgot
If you want to use a Stream more than once, you need to “rewind” it. Use the Seek function to do that
myStream.Seek(0, SeekOrigin.Begin);
The camera can take time to initialize
  Communicate to your user somehow that the camera is ready